## Slide 1
JINDAL STAINLESS | STAINLESS SPARK: ENGINEERING INNOVATION, BUILDING FUTURES | ROUND 2 | PROBLEM STATEMENT 1
Catch every strip defect where it is born, not where it is shipped
AI surface inspection for stainless strip that detects, classifies and scores every defect at line speed, then routes it to the process that caused it. Built, validated on three public steel datasets, and running live today.
0.764
mAP50 on a held-out test split,
joint model (published: 0.70-0.80)
93.7% to 32.5%
clean steel wrongly flagged,
before vs after clean-strip training
INR 2.5-4.2 cr
per line, estimated, vs USD 1-3M
for a commercial system
~2.2 years
payback for one line at a
conservative 1% downgrade rate
TRY THE LIVE DEMO
surface-vision.github.io
The trained detector runs in your browser. Upload a strip image to get box, type, confidence and severity. Nothing leaves the page.
1 Problem
Where is value lost?
2 Insights
What did we learn?
3 Solution
What do we build?
4 Implementation
How does JSL deploy it?
5 Impact
What is it worth?
TEAM [TEAM NAME] | [Member 1] · [Member 2] · [Member 3] · [Member 4] | [INSTITUTION]
Notes: Cover. Open by pointing at the QR: the detector is live at surface-vision.github.io and runs in the judge's browser. The four numbers are the story in one line: it is accurate within the published band, we fixed the false-alarm problem on real clean steel, it costs a fraction of a commercial system, and one line pays back in about two years even at a conservative downgrade rate.

## Slide 2
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
A defect born at the caster is paid for at every later stage, but today it is found at the end of the line
The problem is not that defects exist. They are found late and by sampling, and nobody is told which process caused them.
Sources: AMETEK Surface Vision, Ternium case study (2020); IISE, Measuring the Cost of Quality; ASTM A240 (304: 8.0-10.5% Ni); LME nickel USD 16,402/t and INR 95.8/USD, 22 Sep 2026; JSL FY26 results.
Where stainless surface defects are born, and where they are found without automated inspection
BORN HERE
Inclusions, slivers
Melt & cast
SMS
SEEN TODAY
none
BORN HERE
Rolled-in scale, pits, edge cracks
Hot rolling
HSM
SEEN TODAY
none
BORN HERE
Pickling patches, over / under-pickle
Anneal & pickle
HRAP
SEEN TODAY
spot check
BORN HERE
Scratches, roll marks, crazing
Cold rolling
CRM
SEEN TODAY
spot check
BORN HERE
Stains, BA marks, handling scratches
Final anneal / BA
CRAP / BA
SEEN TODAY
visual sample
BORN HERE
Found here or by the customer
Finish & despatch
Slit, cut
SEEN TODAY
visual + claims
Value added keeps rising left to right: melt, rolling, annealing and pickling are all paid for before the coil is graded. "Seen today" is typical practice without automated surface inspection; JSL's own inspection coverage by line is a P0 input.
Cost-of-quality lens (PAF): where AI inspection moves the money
 | Prevention | Appraisal | Internal failure | External failure
Today | Process fixes happen after complaints | Manual, sampled, inspector-dependent | Downgrade, rework, re-pickle, scrap | Customer claims, returns, lost orders
With AI | Typed defect sent to its owner in minutes | 100% of the surface, the same rule on every coil | Caught upstream, before more value is added | Fewer escapes to exposed-finish customers
Output: shift spend from failure costs (right) to appraisal and prevention (left). Cost of poor quality averages ~15% of sales in manufacturing, range 5-35% (IISE).
Why it hurts more on stainless
300 m/min
"...it is impossible for the human eye to inspect the whole surface." AMETEK / Ternium, cold mill
INR 1.26-1.65 lakh
of nickel in every tonne of 304 (8-10.5% Ni). Downgrading it gives away far more value than on carbon steel
2.57 Mt
JSL FY26 sales at INR 1,67,407/t blended realisation, so every 0.1% downgraded is ~2,570 t
Problem statement How might JSL detect, classify and score every surface defect at line speed, early enough to act, and tell the right process owner what caused it?
Notes: Problem. Walk the chain left to right. The key point: a sliver born at the caster is only seen at finishing, after hot rolling, annealing, pickling and cold rolling have all been paid for. Nickel is why this hurts more on stainless: at today's LME price (USD 16,402/t, INR 95.8/USD) there is INR 1.26-1.65 lakh of nickel in every tonne of 304. The PAF table is the framework: AI inspection is an appraisal cost that moves spend out of internal and external failure. The "seen today" row is typical practice; we found no public statement of JSL's inspection coverage, so we ask for it in P0 instead of assuming.

## Slide 3
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
On stainless the surface is the product, so grade, finish and root cause decide which defect matters
Classify, don't just alarm: a typed defect becomes a work order for a named owner. The pilot belongs on a 300-series cold-rolled line.
Sources: ASSDA, 2B/2D/BA finishes; JSL Q1 FY27 earnings call and results (Aug 2026); JSL cold-rolling expansion to 2.67 MTPA; Steel in Translation 2023 (rolled-in scale); Leão et al. 2021 (tundish slivers). Matrix: team hypothesis.
Three facts that change the brief
1
The finish cannot be repaired
For mill finishes like 2B and BA, "surface damage such as scratches, grinding marks or spatter cannot be matched by polishing" (ASSDA).
2
JSL is moving toward surface-critical tonnes
Cold rolling grows 2.05 to 2.67 MTPA by FY28. The 300-series mix held margins in Q1 FY27. Exports are 11% (Japan, Korea, Brazil).
3
End markets see the surface
Automotive, railways, metros and white goods drive demand (Q1 FY27 call). BA goes into appliance interiors.
Framework: grade-by-defect risk matrix (which defects to train for first)
Grade family | Slivers, inclusions | Scale, pickling | Scratches, roll marks | Edge cracks | Ridging, roping | Typical exposed use
200 series (Cr-Mn) | M | M | H | M | L | Kitchenware, tubes
300 series (304, 316) | H | M | H | L | L | Appliances, auto, rail
400 series (409, 430) | H | M | M | M | H | Exhaust, white goods
Duplex (2205) | M | H | M | H | L | Process, infrastructure
H / M / L = relative surface risk. Team hypothesis from metallurgy literature (e.g. TiN-cluster slivers in Ti-stabilised grades, ridging in ferritic 430, poor hot ductility in duplex); to be re-scored in P0 against JSL's defect records. Output: 300 series carries the highest risk on exposed finishes and the most nickel per tonne, so it is the pilot grade.
Framework: root-cause routing (condensed fishbone). Each class the model outputs maps to a process owner
Defect family | Born at | Likely cause (evidence) | Owner | First corrective action
Inclusion, sliver | Caster | Low tundish level, mould-flux entrainment, reoxidation (Leão 2021) | SMS | Hold tundish level, review flux; tag the heat ID
Rolled-in scale, pits | Reheat, HSM | Descaler pressure below spec, blocked nozzles (Steel in Translation 2023) | HSM | Keep descaler above ~180 bar, clear nozzles
Patches, pickling marks | HRAP / CRAP | Uneven scale removal; acid concentration, temperature, line speed | Pickling line | Check acid concentration and speed across width
Scratches, roll marks | CRM, handling | Guides, roller tables, roll surface condition, coil handling | CRM / logistics | Inspect guides, trigger roll change
Edge cracks | HSM | Edge cooling, low hot ductility (duplex, ferritic) | HSM | Edge heating and trim practice; needs edge cameras
Notes: Insights, stainless-specific. First, the finish is the product and cannot be polished back. Second, JSL is growing cold rolling by about 30% by FY28 and leaning on the 300 series, so the share of surface-critical tonnes rises. The matrix is our framework for choosing what to train first. It is a hypothesis from the metallurgy literature and we say so; P0 re-scores it with JSL's defect records. Its output is the pilot grade: 300 series. The routing table turns detection into action: every class maps to a process owner and a first corrective action. Crazing and patches attributions are reasoned, not sourced, and need a JSL metallurgist's sign-off.

## Slide 4
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
Our Round 1 build produced four findings, and each one changed the design
The model is the cheap part. JSL's own strip, the resolution spec, and trustworthy confidence decide whether the system works.
All numbers are measured and reproducible from reports/*.json in our repository: NEU-DET held-out test (180 images), Severstal (505 clean + 191 defective held-out frames), benchmark.json, calibration.json, ood_guard.json.
1 A model that has never seen clean steel raises false alarms on it
Chart: 
| Clean frames flagged % | Defect recall % | Cross-domain AUC x100
NEU-DET only | 93.7 | 72 | 60.8
+ Severstal joint training | 32.5 | 86.6 | 95.8
On 505 certified-clean Severstal frames the shipped model flagged 93.7%. Training on real clean and defective strip together cut that to 32.5% and raised in-domain mAP50 from 0.752 to 0.764. Training on clean frames alone does not work: recall collapses to 0.057.
So we: train on JSL's own clean and defective strip before any alarm is trusted (P1 gate).
2 Bigger models and higher resolution did not help
Option tested | mAP50 | Cost | Verdict
YOLOv8n, 256 px | 0.752 | 3.0 M params | Chosen
YOLOv8n + clean strip (joint) | 0.764 | same size | Ready
YOLOv8s (3.7x params) | 0.734 | 3.5x FLOPs | No gain
YOLOv8n retrained, 640 px | 0.734 | 4x pixels | No gain
Test-time augmentation | -0.006 | 2.39x latency | Rejected
Held-out split scored once. Nano vs small 95% CI [-0.008, +0.042] spans zero.
So we: ship a 6.22 MB nano model and spend the budget on coverage, not model size.
3 Throughput, not the model, sets the hardware bill
3,064
inferences per second to see every 0.2 mm pixel of a 1.28 m strip at 250 m/min: about 18 accelerators of the class we measured (range 16-19)
48
per second if each camera frame is downscaled to 1.28 mm per pixel: one accelerator, but fine scratches and crazing fall below one pixel
So we: treat resolution as a P0 specification decision with JSL, and size the edge GPUs from it.
4 Operators only act on alarms they can trust
0.142 to 0.046
calibration error (ECE) after isotonic calibration, down 68%. Before it, a box marked "0.60" was right 84% of the time
0 of 3,200
real steel frames wrongly rejected by our out-of-distribution gate, which blocks non-steel images (the raw model scored a white square as a 0.74 "pit")
So we: give every alarm a calibrated confidence and a "this is steel" check before it reaches the HMI.
Notes: Four findings from our own experiments. One: domain shift is the real risk. On real clean steel the NEU-DET-only model flagged 93.7% of frames; joint training on Severstal positives and negatives brought that to 32.5% and AUC from 0.608 to 0.958, with no loss in-domain. Two: we tested bigger models, 640 px and TTA, and none helped. Three: the throughput arithmetic is the real bill: 3,064 inferences a second at 250 m/min at full resolution. The accelerator count is for the laptop-class GPU we measured; a data-centre GPU will need fewer, sized in P0. Four: calibration and the OOD gate are what make alarms trustworthy.

## Slide 5
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
Detect at the tile, decide at the coil, route to the owner, and learn from every operator override
Buy proven optics, own the model. JSL gets vendor-grade capture with a detector trained on its own grades and wired to its own process owners.
BUILT = running in our code today (548 tests; live at surface-vision.github.io). Self-supervised result: J. Mater. Inf. 2025 (SimSiam 0.768 vs ImageNet 0.773 mAP50 on steel). Commercial price range: industry, unverified.
Architecture: six stages from camera to corrective action
1 Capture
Line-scan cameras on both faces, bright- and dark-field light, 0.2 mm/px, encoder-synced
TO BUILD
>
2 Gate
Out-of-distribution and exposure check; rejects non-steel and blown frames
BUILT
>
3 Detect
YOLOv8n joint model on 64 tiles per frame; browser ONNX matches Python 40/40 detections
BUILT
>
4 Score
Calibrated confidence, severity 0-100, defect type and position on the coil map
BUILT
>
5 Decide
Coil ACCEPT / DOWNGRADE / HOLD rules; grade- and finish-specific limits
PARTIAL
>
6 Act & learn
HMI alert, PLC hold, MES coil record, owner work order; overrides feed retraining (0.6 h)
TO BUILD
What is new beyond a standard detector
1
Clean-strip joint training
Fixes the false-alarm failure that kills pilots. Measured: 93.7% to 32.5%.
2
Root-cause routing
Each class maps to an owner (slide 3), so an alarm becomes a work order, not just a red light.
3
Unclassified-defect channel
Anomaly model (PatchCore-type) in parallel for defects never labelled. Proposed.
4
Learn from JSL's unlabelled coils
Self-supervised pretraining matched ImageNet (0.768 vs 0.773) with zero labels in published steel work.
Framework: build vs buy (options scored against JSL's needs)
Capex per line
Proven at line speed
Tuned to JSL grades
Root-cause routing
JSL owns data and model
Time to first line
Commercial (ISRA, AMETEK)
USD 1-3M (unverified)
Fully in-house
INR 2-3 cr (est.)
Hybrid: buy optics, own model
INR 2.5-4.2 cr (est.)
strong
partial
weak
Output: hybrid wins on 4 of 6 criteria and is never weak.
Notes: Solution. Stages 2 to 4 are built and running today, including in the browser demo. Stage 5 has coil rules built, but grade- and finish-specific limits need JSL input. Stages 1 and 6 are plant-side and are the pilot work. The innovations are what make this more than a benchmark model: clean-strip training, root-cause routing, an anomaly channel for unlabelled defects, and self-supervised learning from JSL's own unlabelled coil images. Build vs buy: commercial systems are proven but cost USD 1-3M per line (industry range, unverified) and keep the model closed. Fully in-house is cheapest but takes longest to prove. Hybrid, meaning industrial cameras and lighting plus our model, is never weak on any criterion.

## Slide 6
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
Seven months to shadow mode on one line, and nothing touches the mill until trust is earned
Commit INR 2.5-4.2 cr and one line for seven months. The month-7 go/no-go is decided on JSL's own alarm and recall numbers.
Bill of materials is a team estimate at INR 95.8/USD for a 1.3-1.6 m, two-face installation, to be replaced by vendor quotes in P0. Retrain time 0.6 h measured (15.24 s/epoch x 135 epochs).
Stage-gate roadmap (months)
m0
m4
m8
m12
m16
m20
P0
Instrument one line
Frames at line speed; resolution and grade matrix fixed
P1
Fine-tune on JSL strip
Clean-strip alarms <= 25%, recall >= 90%
P2
Shadow mode, no interlock
>= 90% operator agreement over 4 weeks
P3
PLC hold on severe defects
Holds trusted; downgrade rate measured
P4
Second line and grade
Fleet rollout decision on real payback
pilot go / no-go
EXIT GATE
Cost per line, estimated (INR lakh)
Item | Qty | INR lakh
Line-scan cameras and optics | 8 | 60-95
LED lighting, bright + dark field | 8 | 25-50
Edge GPU servers | 2-3 | 45-75
Enclosures, cooling, encoder, network | 1 set | 30-50
PLC / L2 / MES integration, commissioning | 1 | 60-100
Labelling and fine-tuning (P1) | 5,000 frames | 30-50
Total capex |  | 250-420
Run cost: 2 engineers, spares, support | per year | ~50
Plant integration: read-only first, interlock last
L3 MES / quality
Coil record, disposition, defect map for the customer certificate
P2
L2 Process data
Coil ID, grade, gauge, speed via OPC UA; joins each defect to its heat
P0
L1 PLC
Slow or hold on severe defects; the only write path, enabled in P3
P3
Who does what (RACI)
Activity | JSL Quality | JSL Automation | Line ops | Metallurgy | Project team
Install cameras, line access | C | A | R | I | R
Label frames, fix grade matrix | A | I | C | R | R
Train, calibrate, run model | C | C | I | C | A
PLC / MES integration | C | A | C | I | R
Go / no-go at each gate | A | C | C | C | R
Notes: Implementation. Five phases, 20 months, with a hard go/no-go at month 7 after shadow mode. The mill is never touched by the system until P3; everything before that is read-only. The cost table is our estimate, around INR 2.5-4.2 crore per line, against a commercial range of USD 1-3M, which is about INR 9.6-28.7 crore. We will replace the estimate with vendor quotes in P0. The RACI keeps JSL Quality accountable for every go/no-go.

## Slide 7
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
Every high risk is retired in P0-P2, before any interlock can slow the mill
Feasibility is proven where it can be off-site (accuracy, speed, calibration). What only JSL's line can prove is measured in shadow mode first.
Evidence column from our measured reports (AP50 per class on NEU-DET and GC10 held-out sets). KPI targets are proposed pilot targets, to be agreed with JSL Quality in P0.
Risk map (likelihood x impact)
LIKELIHOOD
High
Med
Low
Low
Med
High
IMPACT
1
2
3
4
5
6
7
Risks, evidence and how each is retired
# | Risk | Evidence | Mitigation | Retired in
1 | Model does not transfer to JSL strip | 93.7% false alarms before joint training | Fine-tune on JSL clean + defect frames | P1
2 | Low-contrast defects missed | Rolled-in scale AP50 0.63 | Dark-field lighting; resolution spec | P0-P1
3 | Rare classes under-learnt | Roll marks AP50 0.20; no edge-crack data | Edge cameras, active learning, anomaly channel | P1-P3
4 | Operators ignore alarms | Uncalibrated scores mislead (ECE 0.142) | Calibrated scores; shadow mode; override log | P2
5 | Compute short at line speed | 3,064 inferences/s at 250 m/min | Benchmark target GPU on real frames | P0
6 | Heat, dust, acid fumes | Pickling and HSM environments | Sealed enclosures, air knives, cooling | P0
7 | PLC / MES integration slips | Plant IT change control | Read-only until P3; one write path | P3
Pilot KPIs: how JSL will know it works
>= 90%
defective frames flagged
measured 92.2% on NEU-DET
<= 25%
clean-strip alarm rate at P1 exit
measured 32.5% on Severstal
<= 0.05
calibration error (ECE)
measured 0.046
<= 200 ms
defect-to-HMI latency
design budget
>= 90%
operator agreement, shadow mode
measured in P2
< 8 h
retrain for a new line or grade
measured 0.6 h
Notes: Feasibility and risk. The top-right of the map is domain transfer and low-contrast defects; both are retired in P0 and P1, before any money is spent on integration. The honest gap is the clean-strip alarm rate: we measured 32.5% on Severstal against a 25% P1 target, which is exactly why P1 fine-tunes on JSL's own strip. Rare classes like roll marks (AP50 0.20) and edge cracks need JSL data and edge cameras; the anomaly channel covers what is never labelled.

## Slide 8
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
At a conservative 1% downgrade rate one line pays back in ~2.2 years; the fleet protects ~INR 13 cr a year
Recommendation: approve a 7-month pilot on one 300-series cold-rolled line. The number that decides fleet rollout is JSL's own downgrade rate.
Inputs: JSL FY26 (INR 1,67,407/t; 25,65,902 t). Swept assumptions: 0.4 Mt line, 30% recovered, INR 3.35 cr capex, INR 0.5 cr/yr run cost, 12% rate. Commercial: USD 2M at INR 95.8. MD quote: ET, 16 Jul 2024.
Loss pool per line, INR cr/yr
0.4 Mt x downgrade rate x price discount x INR 1,67,407/t
Downgraded | 10% off | 15% off | 20% off
0.5% of volume | 3.3 | 5.0 | 6.7
1.0% of volume | 6.7 | 10.0 | 13.4
2.0% of volume | 13.4 | 20.1 | 26.8
Outlined: base case, 6.7 cr pool. Recovering 30% = INR 2.0 cr/yr, 1.5 cr net of run cost. Fleet at the same rates (2.57 Mt, ~6.4 lines): INR 43 cr pool, INR 12.9 cr/yr recovered.
What moves payback (years, base 2.2)
Downgrade rate 0.5-2%
0.9-6.6
Share of loss recovered 15-45%
1.3-6.6
Line volume 0.3-0.5 Mt
1.7-3.3
Capex INR 2.5-4.2 cr
1.7-2.8
Price discount 10-20%
0.9-2.2
Downgrade rate and recovery share dominate. Neither is public, so both are measured in P2-P3 before fleet spend.
Base-case payback
Hybrid (ours)
2.2 yr
Commercial system
12.7 yr
+INR 2.1 cr 5-year NPV per line at 12% >= 0.11% of line revenue lost to downgrade (rate x discount) is enough for a 2-year payback
Impact beyond the P&L
Coverage
100% of both faces, the same rule on every coil, instead of sampled grading
Customers
Defect map per coil for auto, rail and appliance buyers; fewer claims on exposed finishes
Process
Typed defects tied to heat and coil IDs give the SMS and HSM root-cause data they lack today
Safety and assets
Severe-defect holds guard against strip breaks, the Ternium business case
Sustainability
Less remelt and re-pickling of downgraded coils saves energy, acid and nickel
People
"AI will not replace; it will instead renew and re-energise." Inspectors move to decisions (JSL MD)
WHAT WE ASK OF JSL
One 300-series cold-rolled line for 7 months
INR 2.5-4.2 cr pilot budget
Downgrade rate by line and grade from the MIS
A metallurgist at 20% to sign off root causes
In return: measured downgrade rate, payback and a go / no-go at month 7
Notes: Impact. We scoped the business case to one line, which is where the capex is spent. At a conservative 1% of volume downgraded at a 10% discount, one 0.4 Mt line loses INR 6.7 crore a year. Recovering 30% of it, less INR 0.5 crore run cost, pays back INR 3.35 crore in about 2.2 years; a commercial system at the same benefit takes about 12.7 years. That is why the hybrid build matters. The tornado shows the two numbers that dominate are the downgrade rate and how much we recover, and neither is public. So the ask is not only budget; it is JSL's own downgrade data, and the pilot is designed to measure it. Across the fleet, the same rates protect about INR 13 crore a year.