## Slide 1
JINDAL STAINLESS | STAINLESS SPARK: ENGINEERING INNOVATION, BUILDING FUTURES | ROUND 2 | PROBLEM STATEMENT 1
Catch every strip defect where it is born, not where it is shipped
AI surface inspection for stainless strip that detects, classifies and scores every defect at line speed, then routes it to the process that caused it. Built, validated on three public steel datasets, and running live today.
0.764
detection accuracy on unseen steel
images (published range 0.70-0.80)
93.7% to 32.5%
clean steel wrongly flagged,
before vs after clean-strip training
INR 2.5-4.2 cr
per line, estimated, vs USD 1-3M
for a commercial system
~2.2 years
payback for one line at a
conservative 1% downgrade rate
TRY THE LIVE DEMO
surface-vision.github.io
The trained detector runs in your browser. Upload a strip image to get box, type, confidence and severity. Nothing leaves the page.
1 Problem
Where is value lost?
2 Insights
What did we learn?
3 Solution
What do we build?
4 Implementation
How does JSL deploy it?
5 Impact
What is it worth?
TEAM [TEAM NAME] | [Member 1] · [Member 2] · [Member 3] · [Member 4] | [INSTITUTION]
Notes: Cover. Open by pointing at the QR: the detector is live at surface-vision.github.io and runs in the judge's browser. The four numbers are the story in one line: it is accurate within the published band, we fixed the false-alarm problem on real clean steel, it costs a fraction of a commercial system, and one line pays back in about two years even at a conservative downgrade rate.

## Slide 2
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
A defect born at the caster is paid for at every later stage, but today it is found at the end of the line
The problem is not that defects exist. They are found late and by sampling, and nobody is told which process caused them.
Sources: AMETEK Surface Vision, Ternium case study (2020); IISE, Measuring the Cost of Quality; ASTM A240 (304: 8.0-10.5% Ni); LME nickel USD 16,402/t and INR 95.8/USD, 22 Sep 2026; JSL FY26 results.
Where stainless surface defects are born, and where they are found without automated inspection
BORN HERE
Inclusions, slivers
Melt & cast
SMS
SEEN TODAY
none
BORN HERE
Rolled-in scale, pits, edge cracks
Hot rolling
HSM
SEEN TODAY
none
BORN HERE
Pickling patches, over / under-pickle
Anneal & pickle
HRAP
SEEN TODAY
spot check
BORN HERE
Scratches, roll marks, crazing
Cold rolling
CRM
SEEN TODAY
spot check
BORN HERE
Stains, BA marks, handling scratches
Final anneal / BA
CRAP / BA
SEEN TODAY
visual sample
BORN HERE
Found here or by the customer
Finish & despatch
Slit, cut
SEEN TODAY
visual + claims
Value added keeps rising left to right: melt, rolling, annealing and pickling are all paid for before the coil is graded. "Seen today" is typical practice without automated surface inspection; JSL's own inspection coverage by line is a P0 input.
Cost-of-quality lens (PAF): where AI inspection moves the money
 | Prevention | Appraisal | Internal failure | External failure
Today | Process fixes happen after complaints | Manual, sampled, inspector-dependent | Downgrade, rework, re-pickle, scrap | Customer claims, returns, lost orders
With AI | Typed defect sent to its owner in minutes | 100% of the surface, the same rule on every coil | Caught upstream, before more value is added | Fewer escapes to exposed-finish customers
Output: shift spend from failure costs (right) to appraisal and prevention (left). Cost of poor quality averages ~15% of sales in manufacturing, range 5-35% (IISE).
Why it hurts more on stainless
300 m/min
"...it is impossible for the human eye to inspect the whole surface." AMETEK / Ternium, cold mill
INR 1.26-1.65 lakh
of nickel in every tonne of 304 (8-10.5% Ni). Downgrading it gives away far more value than on carbon steel
2.57 Mt
JSL FY26 sales at INR 1,67,407/t blended realisation, so every 0.1% downgraded is ~2,570 t
Problem statement How might JSL detect, classify and score every surface defect at line speed, early enough to act, and tell the right process owner what caused it?
Notes: Problem. Walk the chain left to right. The key point: a sliver born at the caster is only seen at finishing, after hot rolling, annealing, pickling and cold rolling have all been paid for. Nickel is why this hurts more on stainless: at today's LME price (USD 16,402/t, INR 95.8/USD) there is INR 1.26-1.65 lakh of nickel in every tonne of 304. The PAF table is the framework: AI inspection is an appraisal cost that moves spend out of internal and external failure. The "seen today" row is typical practice; we found no public statement of JSL's inspection coverage, so we ask for it in P0 instead of assuming.

## Slide 3
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
On stainless the surface is the product, so grade, finish and root cause decide which defect matters
Classify, don't just alarm: a typed defect becomes a work order for a named owner. The pilot belongs on a 300-series cold-rolled line.
Sources: ASSDA, 2B/2D/BA finishes; JSL Q1 FY27 earnings call and results (Aug 2026); JSL cold-rolling expansion to 2.67 MTPA; Steel in Translation 2023 (rolled-in scale); Leão et al. 2021 (tundish slivers). Matrix: team hypothesis.
Three facts that change the brief
1
The finish cannot be repaired
For mill finishes like 2B and BA, "surface damage such as scratches, grinding marks or spatter cannot be matched by polishing" (ASSDA).
2
JSL is moving toward surface-critical tonnes
Cold rolling grows 2.05 to 2.67 MTPA by FY28. The 300-series mix held margins in Q1 FY27. Exports are 11% (Japan, Korea, Brazil).
3
End markets see the surface
Automotive, railways, metros and white goods drive demand (Q1 FY27 call). BA goes into appliance interiors.
Framework: grade-by-defect risk matrix (which defects to train for first)
Grade family | Slivers, inclusions | Scale, pickling | Scratches, roll marks | Edge cracks | Ridging, roping | Typical exposed use
200 series (Cr-Mn) | M | M | H | M | L | Kitchenware, tubes
300 series (304, 316) | H | M | H | L | L | Appliances, auto, rail
400 series (409, 430) | H | M | M | M | H | Exhaust, white goods
Duplex (2205) | M | H | M | H | L | Process, infrastructure
H / M / L = relative surface risk. Team hypothesis from metallurgy literature (e.g. TiN-cluster slivers in Ti-stabilised grades, ridging in ferritic 430, poor hot ductility in duplex); to be re-scored in P0 against JSL's defect records. Output: 300 series carries the highest risk on exposed finishes and the most nickel per tonne, so it is the pilot grade.
Framework: root-cause routing (condensed fishbone). Each class the model outputs maps to a process owner
Defect family | Born at | Likely cause (evidence) | Owner | First corrective action
Inclusion, sliver | Caster | Low tundish level, mould-flux entrainment, reoxidation (Leão 2021) | SMS | Hold tundish level, review flux; tag the heat ID
Rolled-in scale, pits | Reheat, HSM | Descaler pressure below spec, blocked nozzles (Steel in Translation 2023) | HSM | Keep descaler above ~180 bar, clear nozzles
Patches, pickling marks | HRAP / CRAP | Uneven scale removal; acid concentration, temperature, line speed | Pickling line | Check acid concentration and speed across width
Scratches, roll marks | CRM, handling | Guides, roller tables, roll surface condition, coil handling | CRM / logistics | Inspect guides, trigger roll change
Edge cracks | HSM | Edge cooling, low hot ductility (duplex, ferritic) | HSM | Edge heating and trim practice; needs edge cameras
Notes: Insights, stainless-specific. First, the finish is the product and cannot be polished back. Second, JSL is growing cold rolling by about 30% by FY28 and leaning on the 300 series, so the share of surface-critical tonnes rises. The matrix is our framework for choosing what to train first. It is a hypothesis from the metallurgy literature and we say so; P0 re-scores it with JSL's defect records. Its output is the pilot grade: 300 series. The routing table turns detection into action: every class maps to a process owner and a first corrective action. Crazing and patches attributions are reasoned, not sourced, and need a JSL metallurgist's sign-off.

## Slide 4
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
Our Round 1 build produced four findings, and each one changed the design
The model is the cheap part. JSL's own strip, the resolution spec, and trustworthy confidence decide whether the system works.
All numbers measured by us on three public steel-surface datasets, on images the model never saw in training.
1 A model that has never seen clean steel raises false alarms on it
Chart: 
| Clean strip flagged % | Defects caught % | Clean vs defect separation
Trained on defects only | 93.7 | 72 | 60.8
+ clean strip added | 32.5 | 86.6 | 95.8
On 505 certified-clean steel images, a model trained only on defects flagged 93.7% as defective. Adding real clean strip to training cut that to 32.5%, and accuracy went up, not down. Training on clean strip alone fails: it stops finding defects.
So we: train on JSL's own clean and defective strip before any alarm is trusted.
2 A bigger model or sharper images did not help
Option tested | Accuracy | Extra cost | Verdict
Compact model | 0.752 | - | Chosen
Compact model + clean strip | 0.764 | none | Ready
Model 3.7x larger | 0.734 | 3.5x compute | No gain
4x sharper input images | 0.734 | 4x pixels | No gain
Extra processing per image | 0.006 lower | 2.4x slower | Rejected
Accuracy on held-out images. The gap between compact and large models is within noise.
So we: keep the model compact and spend the budget on camera coverage instead.
3 Line speed, not the model, sets the hardware bill
~18
processors needed to see every 0.2 mm of a 1.28 m wide strip moving at 250 m/min
1
processor is enough if images are coarsened to 1.28 mm, but fine scratches and crazing then disappear
So we: fix the image resolution with JSL at the start, and size the hardware from it.
4 Operators only act on alarms they can trust
68% lower
confidence error after calibration. Before, an alarm marked "60% sure" was right 84% of the time; now stated confidence is within ~5 points of reality
0 of 3,200
real steel images wrongly rejected by our "is this steel?" check, which stops the system judging anything else (unchecked, it called a plain white square a defect)
So we: give every alarm a trustworthy confidence and a "this is steel" check.
Notes: Four findings from our own tests, each of which changed the design. One: a model trained only on defect images treats almost all clean steel as defective, 93.7%. Adding real clean strip cut that to 32.5% and accuracy went up. Two: a bigger model and sharper images did not improve accuracy, so the money goes into cameras, not model size. Three: at full detail a 250 m/min line needs about 18 processors; resolution is therefore a spec decision we make with JSL on day one. Four: operators act only on alarms they trust, so every alarm carries a calibrated confidence and passes an is-this-steel check.

## Slide 5
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
Detect on the strip, decide at the coil, route to the owner, and learn from every operator correction
Buy proven optics, own the model. JSL gets vendor-grade capture with a detector trained on its own grades and wired to its own process owners.
BUILT = working in our prototype today, live at surface-vision.github.io. Unlabelled-learning result: J. Mater. Inf. 2025. Commercial price range: industry figure, unverified.
Architecture: six stages from camera to corrective action
1 Capture
Cameras on both faces of the strip, lit to reveal fine scratches, down to 0.2 mm
TO BUILD
>
2 Check
Confirms the image is usable steel before judging it
BUILT
>
3 Detect
Finds and classifies every defect across the full strip width
BUILT
>
4 Score
Trustworthy confidence, severity 0-100, defect type and position on the coil map
BUILT
>
5 Decide
Coil ACCEPT / DOWNGRADE / HOLD, with limits set per grade and finish
PARTIAL
>
6 Act & learn
Operator alert, coil hold, owner work order; corrections retrain it in under an hour
TO BUILD
What is new beyond a standard detector
1
Trained on clean strip, not just defects
Fixes the false-alarm problem that kills most pilots. Measured: 93.7% to 32.5%.
2
Root-cause routing
Each class maps to an owner (slide 3), so an alarm becomes a work order, not just a red light.
3
Catches defects it was never taught
A second check flags unusual surface patterns that were never labelled. Proposed.
4
Learns from JSL's unlabelled coils
Published steel research shows unlabelled images train as well as the standard approach, so JSL's image archive becomes an asset.
Framework: build vs buy (options scored against JSL's needs)
Capex per line
Proven at line speed
Tuned to JSL grades
Root-cause routing
JSL owns data and model
Time to first line
Commercial (ISRA, AMETEK)
USD 1-3M (unverified)
Fully in-house
INR 2-3 cr (est.)
Hybrid: buy optics, own model
INR 2.5-4.2 cr (est.)
strong
partial
weak
Output: hybrid wins on 4 of 6 criteria and is never weak.
Notes: Solution. Stages 2 to 4 are built and running today, including in the browser demo. Stage 5 has coil rules built, but grade- and finish-specific limits need JSL input. Stages 1 and 6 are plant-side and are the pilot work. What makes this more than a standard detector: it is trained on clean strip as well as defects, every defect is routed to the process that caused it, a second check catches defects it was never taught, and it can learn from JSL's unlabelled image archive. Build vs buy: commercial systems are proven but cost USD 1-3M per line and keep the model closed. Fully in-house is cheapest but slowest to prove. Hybrid, meaning industrial cameras plus our model, is never weak on any criterion.

## Slide 6
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
Seven months to shadow mode on one line, and nothing touches the mill until trust is earned
Commit INR 2.5-4.2 cr and one line for seven months. The month-7 go/no-go is decided on JSL's own alarm and recall numbers.
Costs are team estimates for a 1.3-1.6 m line inspected on both faces, at INR 95.8/USD; to be replaced by vendor quotes in P0.
Stage-gate roadmap (months)
m0
m4
m8
m12
m16
m20
P0
Instrument one line
Frames at line speed; resolution and grade matrix fixed
P1
Fine-tune on JSL strip
Clean-strip alarms <= 25%, recall >= 90%
P2
Shadow mode: advises only
>= 90% operator agreement over 4 weeks
P3
Auto-hold on severe defects
Holds trusted; downgrade rate measured
P4
Second line and grade
Fleet rollout decision on real payback
pilot go / no-go
EXIT GATE
Cost per line, estimated (INR lakh)
Item | INR lakh
Cameras and lighting | 85-145
Computing hardware | 45-75
Installation and plant integration | 90-150
Training on JSL's own strip | 30-50
Total, one line | 250-420
Running cost, per year | ~50
Plant connection: read-only first, control last
Process data
from P0
Coil ID, grade, gauge and speed, so each defect is tied to the heat it came from
>
Quality records
from P2
Coil disposition and a defect map that can travel with the customer certificate
>
Line control
from P3
Slow or hold the line on severe defects. The only write path, switched on last
Notes: Implementation. Five phases, 20 months, with a hard go/no-go at month 7 after shadow mode. The system never acts on the mill until P3; before that it only reads data and advises. Cost is our estimate, INR 2.5-4.2 crore per line, against a commercial range of USD 1-3M, about INR 9.6-28.7 crore. Vendor quotes replace the estimate in P0. The plant connection goes in order: process data first, quality records next, line control last.

## Slide 7
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
Every high risk is retired in P0-P2, before the system is allowed to slow the mill
Accuracy, speed and trust are already proven off-site. What only JSL's line can prove is measured in shadow mode first.
Evidence from our own tests on public steel datasets. KPI targets are proposed, to be agreed with JSL Quality in P0.
Risk map (likelihood x impact)
LIKELIHOOD
High
Med
Low
Low
Med
High
IMPACT
1
2
3
4
5
6
7
Risks, evidence and how each is retired
# | Risk | Evidence | Mitigation | Retired in
1 | Model does not transfer to JSL strip | 93.7% false alarms before the fix | Train on JSL clean and defect images | P1
2 | Low-contrast defects missed | Rolled-in scale is our weakest class | Angled lighting; sharper images | P0-P1
3 | Rare defects under-learnt | Few roll-mark or edge-crack examples | Edge cameras; targeted labelling | P1-P3
4 | Operators ignore alarms | Raw confidence was over-confident | Calibrated scores; shadow mode; override log | P2
5 | Not enough computing at line speed | ~18 processors needed at full detail | Test target hardware on real frames | P0
6 | Heat, dust, acid fumes | Pickling and HSM environments | Sealed enclosures, air knives, cooling | P0
7 | Plant IT integration slips | Plant IT change control | Read-only until P3; one write path | P3
Pilot KPIs: how JSL will know it works
>= 90%
defective strip flagged
measured 92.2% in our tests
<= 25%
clean strip wrongly flagged
measured 32.5% in our tests
<= 5 pts
gap between stated and real confidence
measured 4.6 pts
< 0.2 s
from defect to operator screen
design target
>= 90%
operator agreement, shadow mode
measured in P2
< 8 h
to retrain for a new line or grade
measured 0.6 h
Notes: Feasibility and risk. The top-right of the map is transfer to JSL strip and low-contrast defects; both are retired in P0 and P1, before money is spent on integration. The honest gap is clean strip wrongly flagged: we measured 32.5% against a 25% target, which is exactly why P1 trains on JSL's own strip. Rare defects like roll marks and edge cracks need JSL data and edge cameras; the unseen-defect check covers what is never labelled.

## Slide 8
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | [TEAM NAME]
At a conservative 1% downgrade rate one line pays back in ~2.2 years; the fleet protects ~INR 13 cr a year
Recommendation: approve a 7-month pilot on one 300-series cold-rolled line. The number that decides fleet rollout is JSL's own downgrade rate.
Inputs: JSL FY26 (INR 1,67,407/t; 25,65,902 t). Swept assumptions: 0.4 Mt line, 30% recovered, INR 3.35 cr capex, INR 0.5 cr/yr run cost, 12% rate. Commercial: USD 2M at INR 95.8. MD quote: ET, 16 Jul 2024.
Loss pool per line, INR cr/yr
0.4 Mt x downgrade rate x price discount x INR 1,67,407/t
Downgraded | 10% off | 15% off | 20% off
0.5% of volume | 3.3 | 5.0 | 6.7
1.0% of volume | 6.7 | 10.0 | 13.4
2.0% of volume | 13.4 | 20.1 | 26.8
Outlined: base case, 6.7 cr pool. Recovering 30% = INR 2.0 cr/yr, 1.5 cr net of run cost. Fleet at the same rates (2.57 Mt, ~6.4 lines): INR 43 cr pool, INR 12.9 cr/yr recovered.
What moves payback (years, base 2.2)
Downgrade rate 0.5-2%
0.9-6.6
Share of loss recovered 15-45%
1.3-6.6
Line volume 0.3-0.5 Mt
1.7-3.3
Capex INR 2.5-4.2 cr
1.7-2.8
Price discount 10-20%
0.9-2.2
Downgrade rate and recovery share dominate. Neither is public, so both are measured in P2-P3 before fleet spend.
Base-case payback
Hybrid (ours)
2.2 yr
Commercial system
12.7 yr
+INR 2.1 cr 5-year NPV per line at 12% >= 0.11% of line revenue lost to downgrade (rate x discount) is enough for a 2-year payback
Impact beyond the P&L
Coverage
100% of both faces, the same rule on every coil, instead of sampled grading
Customers
Defect map per coil for auto, rail and appliance buyers; fewer claims on exposed finishes
Process
Typed defects tied to heat and coil IDs give the SMS and HSM root-cause data they lack today
Safety and assets
Severe-defect holds guard against strip breaks, the Ternium business case
Sustainability
Less remelt and re-pickling of downgraded coils saves energy, acid and nickel
People
"AI will not replace; it will instead renew and re-energise." Inspectors move to decisions (JSL MD)
WHAT WE ASK OF JSL
One 300-series cold-rolled line for 7 months
INR 2.5-4.2 cr pilot budget
Downgrade rate by line and grade from the MIS
A metallurgist at 20% to sign off root causes
In return: measured downgrade rate, payback and a go / no-go at month 7
Notes: Impact. We scoped the business case to one line, which is where the capex is spent. At a conservative 1% of volume downgraded at a 10% discount, one 0.4 Mt line loses INR 6.7 crore a year. Recovering 30% of it, less INR 0.5 crore run cost, pays back INR 3.35 crore in about 2.2 years; a commercial system at the same benefit takes about 12.7 years. That is why the hybrid build matters. The tornado shows the two numbers that dominate are the downgrade rate and how much we recover, and neither is public. So the ask is not only budget; it is JSL's own downgrade data, and the pilot is designed to measure it. Across the fleet, the same rates protect about INR 13 crore a year.