## Slide 1
JINDAL STAINLESS | STAINLESS SPARK | ROUND 2 | PROBLEM STATEMENT 1
Catch every strip defect where it is born, not where it is shipped
AI surface inspection that finds, grades and routes every stainless strip defect to the process that caused it.
90%
of defects caught on real mill
strip it had never seen
4.7%
of clean strip wrongly flagged,
fewer than 1 in 20
₹2.5-4.2 cr
per line, vs ₹10-29 cr for a
commercial system
~2.2 years
payback on one line at a
1% downgrade rate
REAL DETECTIONS BY OUR MODEL, ON STEEL IMAGES IT NEVER SAW IN TRAINING
Prathmesh Walimbe · Krishna Kanta Mondal | IIT Bombay
TRY THE LIVE DEMO
surface-vision.github.io
Runs in your browser. Nothing leaves the page.
Photo: Methem, Wikimedia Commons (public domain)
Notes: Cover. The strip of six images is real output from our model on held-out steel images. The QR opens the live demo, which runs in the judge's browser. Four numbers tell the story: on real mill strip it catches 9 in 10 defects and wrongly flags fewer than 1 in 20 clean images, at a fraction of commercial cost, paying back in about two years on one line.

## Slide 2
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | IIT Bombay
A defect born at the caster is paid for at every later stage, but today it is found only at the end
The problem is not that defects exist. They are found late, by sampling, and nobody is told which process caused them.
Sources: AMETEK/Ternium (2020); ASSDA; IISE; ASTM A240; LME nickel USD 16,402/t at INR 95.8/USD (22 Sep 2026); ISSDA (FY25); DGTR (29 Sep 2025); BIS Steel QCO 2024; JSL.
Where stainless surface defects are born, and where they are seen today
VALUE ADDED KEEPS RISING →
Melt & cast
SMS
Inclusions, slivers
NOT SEEN
Hot rolling
HSM
Scale, pits, edge cracks
NOT SEEN
Anneal & pickle
HRAP
Pickling patches
SPOT CHECK
Cold rolling
CRM
Scratches, roll marks
SPOT CHECK
Final anneal / BA
CRAP / BA
Stains, BA marks
SAMPLED
Finish & despatch
Slit, cut
Found here, or by the customer
CLAIMS
Why it hurts more on stainless
300 m/min
too fast for the eye to see the whole surface
₹126k-165k
of nickel in every tonne of 304, given away on a downgrade
No repair
damage on 2B/BA mill finishes cannot be polished out
Why now
India demand, Mt +84% in 5 yrs
Chart: 
| FY21 | FY22 | FY23 | FY24 | FY25 | FY30F
Actual | 2.61 | 3.46 | 3.94 | 4.49 | 4.8 | 0
Forecast | 0 | 0 | 0 | 0 | 0 | 6.8
1.73 Mt imports
FY25; anti-dumping probe on cold-rolled 300/400, Sep 2025
IS 6911 mandatory
BIS certification for sheet and strip, since Aug 2024
2.67 MTPA
JSL cold rolling by FY28, up from 2.05
Cost of quality: where AI moves the money
spend moves from failure to prevention
Prevention
defect sent to its owner in minutes
Internal failure
caught before more value is added
Appraisal
100% of the surface, every coil
External failure
fewer escapes to customers
Poor quality costs ~15% of sales in manufacturing (IISE).
Notes: Problem. Walk the ribbon left to right: a sliver born at the caster is only seen at finishing, after hot rolling, annealing, pickling and cold rolling have been paid for. Why stainless hurts more: every tonne of 304 carries INR 126,000-165,000 of nickel, and a 2B or BA mill finish cannot be polished back. Why now: Indian stainless demand grew 84% in five years to 4.8 Mt and is heading to 6.8 Mt by FY30, led by rail and metro coaches; imports hit 1.73 Mt in FY25 and DGTR opened an anti-dumping probe on cold-rolled 300/400 series in September 2025, so quality is the domestic producer's moat; BIS certification to IS 6911 has been mandatory for sheet and strip since August 2024; and JSL is adding cold-rolling capacity. The cost-of-quality frame is the output: inspection moves spend from failure to prevention.

## Slide 3
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | IIT Bombay
On stainless the surface is the product, so every defect type must reach the process that caused it
Classify, don't just alarm: a typed defect becomes a work order for a named owner. The pilot belongs on 300-series cold-rolled strip.
Images: held-out test frames, boxes by our model. Sources: Nortal/Outokumpu (2024); Tata Steel; Parsytec (Stainless Steel World); Leão 2021; Steel in Translation 2023. Owners, grade risks: team hypotheses.
Six defect families, six different owners (real detections by our model)
Born: Caster
Owner: SMS
Fix: Tundish level, mould flux
Born: Reheat, hot rolling
Owner: HSM
Fix: Reheat and coiling temperature
Born: Hot rolling
Owner: HSM
Fix: Descaler pressure, nozzles
Born: Reheat, pickling
Owner: HSM / pickling
Fix: Furnace atmosphere, over-pickling
Born: Anneal & pickle
Owner: Pickling line
Fix: Acid strength, line speed
Born: Cold rolling, handling
Owner: CRM / logistics
Fix: Guides, rolls, coil handling
Stainless-only types to add with JSL data:
Roping
Ridging (ferritic 430)
Orange peel
Anneal colour
BA stains
Lamination
Precedent: who already does this, and what we copy
Outokumpu
Europe's #1 stainless maker; AI inspection live at Tornio since 2024, runs offline. Copy: offline edge, multi-site
Tata Steel
Kalinganagar (WEF Lighthouse) finds cold-rolled surface defects by video analytics. Copy: in-house model team
Parsytec
On stainless lines: 170 µm cameras, bright + dark-field light, a decision per coil. Copy: optics, coil decision
Grade-by-defect risk: which defects to train for first
Grade | Slivers | Scale | Scratches | Edge cracks | Ridging
200 series (Cr-Mn) | M | M | H | M | L
300 series (304, 316) | H | M | H | L | L
400 series (409, 430) | H | M | M | M | H
Duplex (2205) | M | H | M | H | L
OUTPUT 300 series is the pilot grade: highest exposed-finish risk and the most nickel per tonne.
Notes: Insights, stainless-specific. The six images are our model's real detections on held-out frames; each family is born at a different stage, so a typed detection goes straight to the right owner as a work order. The owner mapping needs a JSL metallurgist's sign-off in P0. Precedent: Outokumpu, Europe's largest stainless producer, switched on an AI surface inspection system at Tornio in October 2024, built to run without internet and scale across sites; Tata Steel Kalinganagar, India's first WEF Lighthouse, uses video analytics for surface defects on cold-rolled products; Parsytec systems on stainless lines use 170 micron cameras with bright and dark field light and make a decision per coil. We copy the offline edge design, an in-house model team, and the optics spec. The grade matrix output is the pilot grade: 300 series.

## Slide 4
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | IIT Bombay
Four design choices behind the system, each proven in our own tests
The model is the cheap part. JSL's own strip, the image resolution and trustworthy confidence decide whether the system works.
All numbers measured by us on three public steel-surface datasets, on images the model never saw in training.
1 Trained on clean steel too, so its alarms mean something
Chart: 
| a | b
of defects caught | 89.6 | 10.4
90%
of defects caught
258 of 288 defective mill images
Chart: 
| a | b
of clean strip flagged | 4.7 | 95.3
4.7%
of clean strip flagged
14 of 300 clean mill images
So we: train on JSL's own clean and defective strip before any alarm is trusted.
2 A compact model is enough
12 MB
the whole model; loads in any browser
~55 ms
per image on an ordinary laptop CPU
0.75
accuracy, inside the 0.70-0.80 published range
Larger models and sharper images added no accuracy in our tests.
So we: keep the model compact and spend the budget on camera coverage.
3 Image detail, not the model, sets the hardware bill
0.2 mm per pixel
~18 processors
sees defects from ~0.5 mm
0.5 mm per pixel
~3 processors
sees defects from ~1.3 mm
1.28 mm per pixel
1 processor
fine scratches vanish (~3 mm)
1.28 m strip at 250 m/min. Processors scale with pixels; a defect needs 2-3 pixels.
So we: fix the image resolution with JSL first, then size the hardware.
4 Operators act only on alarms they can trust
±3 pts
between stated confidence and reality, so a "70%" alarm is right about 70% of the time
0 of 3,200
real steel images wrongly rejected by our "is this steel?" check, which stops the system judging anything else
So we: every alarm carries a trustworthy confidence and a steel check.
Notes: Four findings from our own tests, each of which changed the design. One: because it is trained on clean steel as well as defects, it flags only 14 of 300 clean mill images while catching 258 of 288 real defects. Two: a 12 MB model is enough; larger models and sharper images added no accuracy, so money goes into cameras. Three: at full detail a 250 m/min line needs about 18 processors; resolution is a spec decision we make with JSL on day one. Four: operators act only on alarms they trust, so every alarm carries a calibrated confidence and passes an is-this-steel check.

## Slide 5
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | IIT Bombay
Detect on the strip, decide at the coil, route to the owner, and learn from every correction
Buy proven cameras, own the model: vendor-grade capture with a detector trained on JSL's grades and wired to JSL's process owners.
BUILT = working in our prototype today, live at surface-vision.github.io. Unlabelled-learning result: J. Mater. Inf. 2025. Commercial price range: industry figure, unverified.
How it works: six stages from camera to corrective action
Capture
Both faces, bright + dark-field light, 0.2 mm detail
TO BUILD
Check
Is it usable steel? If not, skip it
BUILT
Detect
Find and classify every defect
BUILT
Score
Confidence, severity 0-100, coil position
BUILT
Decide
Accept, downgrade or hold, per grade
PARTIAL
Act & learn
Alert, hold, work order; corrections retrain it
TO BUILD
At the line: cameras, lights
Edge server beside the line: runs offline, ~55 ms per image
Plant network (IEC 62443)
People: screen, work orders
Running today
Upload a strip image, get: • box on the defect
• defect type
• confidence
• severity score
16 samples built in, including clean mill strip. Or drop your own photo.
surface-vision.github.io runs in the browser
What is new beyond a standard detector
Trained on clean strip too
only 4.7% of clean strip raises an alarm
Root-cause routing
every alarm becomes a work order
Unseen-defect check
flags patterns never labelled (proposed)
Learns from unlabelled coils
JSL's image archive becomes an asset
Build vs buy
Cost per line
Proven at speed
Tuned to JSL grades
JSL owns model
Commercial
USD 1-3M (unverified)
Fully in-house
₹2-3 cr (est.)
Hybrid (recommended)
₹2.5-4.2 cr (est.)
strong
partial
weak
Output: hybrid is never weak.
Notes: Solution. Stages 2 to 4 are built and running today, including in the browser demo. Stage 5 has coil rules built, but grade- and finish-specific limits need JSL input. Stages 1 and 6 are the plant-side pilot work. What makes this more than a standard detector: it is trained on clean strip as well as defects, every defect is routed to the process that caused it, a second check catches defects it was never taught, and it can learn from JSL's unlabelled image archive. Build vs buy: commercial systems are proven but cost USD 1-3M per line and keep the model closed; hybrid is never weak.

## Slide 6
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | IIT Bombay
It already works on public steel data; the pilot's job is to prove it on JSL's own strip
Strong on four of six defect families today. Every weak spot is known, and each has a fix in the pilot plan.
Datasets: NEU-DET (Northeastern Univ.); Severstal steel defects (Kaggle); GC10-DET (Lv et al. 2020, CC BY 4.0). All scores on held-out images the model never saw in training; model chosen on validation across four training runs.
Tested on three public steel datasets
NEU-DET
1,800 images, 6 defect types
University benchmark, hot-rolled strip
Severstal
12,568 real mill frames
Production strip from a steel mill
GC10-DET
2,294 frames, 10 types
Full-width line-scan camera frames (roll marks shown)
How well it finds each defect type (accuracy, held-out images)
published range
Patches
0.94
Inclusion
0.80
Scratches
0.79
Pitted surface
0.76
Rolled-in scale
0.60
Crazing
0.58
Headline results
178 of 180
test images: the right defect type named
~55 ms
per image, running in an ordinary laptop browser
~10,100
Lab 1,800
Mill strip 6,001
Line-scan 2,294
Known weak spots, and the fix for each
Weak spot | Today (0-1) | Fix in the pilot
Low-contrast texture: crazing, rolled-in scale | 0.58-0.60 | Angled lighting; JSL labels in P1
Real mill frames are harder than the lab benchmark | 0.57 vs 0.75 | Train on JSL's own strip in P1
Roll marks and edge cracks: few examples | 0.20 | Edge cameras; synthetic defects; targeted labels
Notes: Proof. Three public datasets, about 10,100 images, all scored on images the model never saw in training. Per defect, four of six families sit at or above the published range; crazing and rolled-in scale are low-contrast textures and are weaker. The honest headline is the second weak spot: on real mill frames accuracy is 0.57 against 0.75 on the lab benchmark. That is exactly why P1 trains on JSL's own strip before anything is trusted. Roll marks score 0.20 on GC10 because there are only a few dozen examples; edge cameras and targeted labelling fix that.

## Slide 7
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | IIT Bombay
Seven months to shadow mode on one line, and nothing touches the mill until trust is earned
Commit ₹2.5-4.2 cr and one line for seven months. The month-7 go/no-go is decided on JSL's own alarm and recall numbers.
Costs: team estimates for a 1.3-1.6 m line, both faces, at INR 95.8/USD; vendor quotes replace them in P0. Pragati: JSL digitalisation, Phase 2 brings Level-2 data at Jajpur.
Stage-gate roadmap (months)
m0
m4
m8
m12
m16
m20
◆ EXIT GATE
P0
Instrument one line
Optics fixed; Pragati L2 data linked
P1
Train on 5,000 JSL frames
Clean alarms ≤ 25%, recall ≥ 90%
P2
Shadow mode: advises only
≥ 90% operator agreement
P3
Auto-hold on severe defects
Holds trusted; downgrade measured
P4
Second line and grade
Fleet decision on real payback
pilot go / no-go
Cost per line, estimated
Chart: 
| Cameras & lighting | Installation & integration | Computing hardware | Training on JSL strip
Cost | 115 | 120 | 60 | 40
₹2.5-4.2
cr per line
Cameras & lighting
₹0.85-1.45 cr
Installation & integration
₹0.9-1.5 cr
Computing hardware
₹0.45-0.75 cr
Training on JSL strip
₹0.3-0.5 cr
Running cost ~₹0.5 cr a year
Commercial system: ₹10-29 cr per line
Top risks, and when each is retired
Risk | Mitigation | Retired
Model does not transfer to JSL strip | Train on JSL clean and defect images | P1
Mirror-like BA/2B finish hides defects | Bright + dark-field light; deflectometry for BA | P0-P1
Rare defects under-learnt | Edge cameras; synthetic defects; targeted labels | P1-P3
Operators ignore alarms | Trusted scores; shadow mode first | P2
Plant network, heat and fumes | IEC 62443 zones, runs offline; sealed enclosures | P0
Quality slips after a model update | Every retrain must beat the live model first | P2+
Pilot KPIs: how JSL will know it works
≥ 90%
defective strip flagged
measured 258 of 288 (89.6%)
≤ 25%
clean strip wrongly flagged
measured 4.7% on mill strip
≤ 5 pts
confidence vs reality gap
measured 3.3 pts
< 0.2 s
defect to operator screen
design target
≥ 90%
operator agreement, shadow
measured in P2
< 8 h
retrain for a new grade
measured 0.6 h
Notes: Implementation. Five phases, 20 months, with a hard go/no-go at month 7 after shadow mode. The system never acts on the mill until P3; before that it only reads data and advises. P0 plugs into Project Pragati, JSL's own digitalisation programme with Dassault Systemes and Capgemini, whose Phase 2 brings Level-2 process data at Jajpur; so each defect is tied to its heat and coil without a new integration project. Mirror-like BA and 2B finishes are handled the way stainless lines already do it: bright and dark-field light, with deflectometry for BA. The plant network is protected by IEC 62443 zones and the system runs offline, as Outokumpu's does. Every retrained model must beat the live one on a fixed JSL test set before it ships. Cost is INR 2.5-4.2 crore per line, against USD 1-3M for a commercial system.

## Slide 8
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
STAINLESS SPARK ROUND 2 | PS1 | IIT Bombay
At a conservative 1% downgrade rate one line pays back in ~2.2 years; the fleet protects ~₹13 cr a year
Recommendation: approve a 7-month pilot on one 300-series cold-rolled line. JSL's own downgrade rate decides fleet rollout.
Inputs: JSL FY26 (INR 167,407/t; 2,565,902 t). Base: 0.4 Mt line, 30% of loss recovered, ₹3.35 cr capex, ₹0.5 cr/yr run cost, 12% rate. Commercial: USD 2M at INR 95.8.
Loss pool per line, ₹ cr a year
0.4 Mt × downgrade rate × price discount × ₹167,407/t
Downgraded | 10% off | 15% off | 20% off
0.5% of volume | 3.3 | 5.0 | 6.7
1.0% of volume | 6.7 | 10.0 | 13.4
2.0% of volume | 13.4 | 20.1 | 26.8
Base case (dark): ₹6.7 cr pool, ₹2.0 cr/yr recovered (₹1.5 cr net). Fleet: ₹12.9 cr/yr. Non-prime coil sells 10-30% below prime, so these discounts are conservative.
Cumulative cash per line, ₹ cr
Y0
-3.4
Y1
-1.8
Y2
-0.3
Y3
+1.2
Y4
+2.7
Y5
+4.2
pays back ~2.2 yr
+₹2.1 cr 5-year NPV per line at 12%
−₹11.6 cr commercial system after 5 years
≥ 0.11% of revenue lost to downgrade = 2-yr payback
What moves payback (years)
Downgrade rate 0.5-2%
0.9-6.6
Share recovered 15-45%
1.3-6.6
Line volume 0.3-0.5 Mt
1.7-3.3
Capex ₹2.5-4.2 cr
1.7-2.8
Price discount 10-20%
0.9-2.2
base 2.2 yr
Impact beyond the P&L
Coverage
100% of both faces, every coil
today: spot checks
Customers
Defect map per coil for rail, metro, auto buyers
Vande Bharat supplier
Process
Defects tied to heat and coil IDs
6 families, 6 owners
Safety
Severe-defect holds prevent strip breaks
Ternium's business case
Sustainability
Less rework and remelt; backs net zero
JSL: 1.76 tCO2e/t, FY26
People
Inspectors move to decisions
HR AI: 95% self-served
WHAT WE ASK OF JSL
One 300-series cold-rolled line, 7 months
₹2.5-4.2 cr pilot budget
Downgrade rate by line and grade
A metallurgist at 20% for root causes
In return: measured downgrade rate, payback and a go / no-go at month 7.
Notes: Impact. At 1% of volume downgraded at a 10% discount, one 0.4 Mt line loses INR 6.7 crore a year; recovering 30%, less INR 0.5 crore run cost, pays back INR 3.35 crore capex in about 2.2 years, against 12.7 years for a commercial system. Our discounts are conservative: non-prime coil typically trades 10-30% below prime. Downgrade rate and recovery share dominate the tornado; neither is public, so both are measured in P2-P3. Beyond the P&L: JSL supplies stainless for Vande Bharat sleeper coaches, Vande Metro and several metros, and those buyers see the surface; a defect map per coil is a sales tool. Less rework and remelting supports JSL's target of halving emission intensity by 2035 and net zero by 2050; intensity was 1.76 tCO2e per tonne in FY26. Close on the ask.