## Slide 1
ROUND 2 · PROBLEM STATEMENT 1
AI surface defect detection
Catch every strip defect where it is born, not where it is shipped
AI surface inspection that finds, grades and routes every stainless strip defect to the process that caused it.
90%
of defects caught on real mill
strip it had never seen
4.7%
of clean strip wrongly flagged,
fewer than 1 in 20
~₹6.7 cr
a year at stake per line, at a
1% downgrade rate
7 months
to shadow mode on one line,
go / no-go at month 7
REAL OUTPUT FROM OUR SYSTEM, ON STEEL IMAGES IT HAD NEVER SEEN
TEAM Futuristic | Krishna Kanta Mondal · Prathmesh Walimbe | IIT Bombay
TRY THE LIVE DEMO
surface-vision.github.io
Runs in your browser. Nothing leaves the page.
Photo: Methem, Wikimedia Commons (public domain)
Notes: Cover. The six images are real output from our system on steel images it had never seen. The QR opens the live demo in the judge's browser. Four numbers tell the story: on real mill strip it catches 9 in 10 defects and wrongly flags fewer than 1 in 20 clean images; each line has about INR 6.7 crore a year at stake from downgrades even at a conservative 1%; and one line reaches shadow mode in seven months, with a go/no-go before anything touches the mill.

## Slide 2
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
Team Futuristic
IIT Bombay
A defect born at the caster is paid for at every later stage, but today it is found only at the end
PROBLEM · WHY NOW
The problem is not that defects exist. They are found late, by sampling, and nobody is told which process caused them.
Sources: AMETEK/Ternium (2020); ASSDA; IISE; ASTM A240; LME nickel USD 16,402/t at INR 95.8/USD (22 Sep 2026); ISSDA (FY25); DGTR (29 Sep 2025); BIS Steel QCO 2024; JSL.
Where stainless surface defects are born, and where they are seen today
VALUE ADDED KEEPS RISING →
Melt & cast
SMS
Inclusions, slivers
NOT SEEN
Hot rolling
HSM
Scale, pits, edge cracks
NOT SEEN
Anneal & pickle
HRAP
Pickling patches
SPOT CHECK
Cold rolling
CRM
Scratches, roll marks
SPOT CHECK
Final anneal / BA
CRAP / BA
Stains, BA marks
SAMPLED
Finish & despatch
Slit, cut
Found here, or by the customer
CLAIMS
Why it hurts more on stainless
300 m/min
too fast for the eye to see the whole surface
₹126k-165k
of nickel in every tonne of 304, given away on a downgrade
No repair
damage on 2B/BA mill finishes cannot be polished out
Why now
India demand, Mt +84% in 5 yrs
Chart: 
| FY21 | FY22 | FY23 | FY24 | FY25 | FY30F
Actual | 2.61 | 3.46 | 3.94 | 4.49 | 4.8 | 0
Forecast | 0 | 0 | 0 | 0 | 0 | 6.8
1.73 Mt imports
FY25; anti-dumping probe on cold-rolled 300/400, Sep 2025
IS 6911 mandatory
BIS certification for sheet and strip, since Aug 2024
2.67 MTPA
JSL cold rolling by FY28, up from 2.05
Cost of quality: where AI moves the money
spend moves from failure to prevention
Prevention
defect sent to its owner in minutes
Internal failure
caught before more value is added
Appraisal
100% of the surface, every coil
External failure
fewer escapes to customers
Poor quality costs ~15% of sales in manufacturing (IISE).
Notes: Problem. Walk the ribbon left to right: a sliver born at the caster is only seen at finishing, after hot rolling, annealing, pickling and cold rolling have been paid for. Why stainless hurts more: every tonne of 304 carries INR 126,000-165,000 of nickel, and a 2B or BA mill finish cannot be polished back. Why now: Indian stainless demand grew 84% in five years to 4.8 Mt and is heading to 6.8 Mt by FY30, led by rail and metro coaches; imports hit 1.73 Mt in FY25 and DGTR opened an anti-dumping probe on cold-rolled 300/400 series in September 2025, so quality is the domestic producer's moat; BIS certification to IS 6911 has been mandatory for sheet and strip since August 2024; and JSL is adding cold-rolling capacity. The cost-of-quality frame is the output: inspection moves spend from failure to prevention.

## Slide 3
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
Team Futuristic
IIT Bombay
On stainless the surface is the product, so every defect type must reach the process that caused it
INSIGHTS · OWNERS · PRECEDENT
Classify, don't just alarm: a typed defect becomes a work order for a named owner. The pilot belongs on 300-series cold-rolled strip.
Images: held-out test frames, boxes drawn by our system. Sources: Nortal/Outokumpu (2024); Tata Steel; Parsytec (Stainless Steel World); Leão 2021; Steel in Translation 2023. Owners: team hypothesis. Grade risks: team hypothesis.
Six defect families, each traced to the process that caused it (real output from our system)
Born: Caster
Owner: SMS
Fix: Tundish level, mould flux
Born: Reheat, hot rolling
Owner: HSM
Fix: Reheat and coiling temperature
Born: Hot rolling
Owner: HSM
Fix: Descaler pressure, nozzles
Born: Reheat, pickling
Owner: HSM / pickling
Fix: Furnace atmosphere, over-pickling
Born: Anneal & pickle
Owner: Pickling line
Fix: Acid strength, line speed
Born: Cold rolling, handling
Owner: CRM / logistics
Fix: Guides, rolls, coil handling
Stainless-only types to add with JSL data:
Roping
Ridging (ferritic 430)
Orange peel
Anneal colour
BA stains
Lamination
Precedent: who already does this, and what we copy
Outokumpu
Europe's #1 stainless maker; AI inspection live at Tornio since 2024, runs offline. Copy: offline edge, multi-site
Tata Steel
Kalinganagar (WEF Lighthouse) finds cold-rolled surface defects by video analytics. Copy: in-house team owns it
Parsytec
On stainless lines: 170 µm cameras, bright + dark-field light, a decision per coil. Copy: optics, coil decision
Grade-by-defect risk: which defects to train for first
Grade | Slivers | Scale | Scratches | Edge cracks | Ridging
200 series (Cr-Mn) | M | M | H | M | L
300 series (304, 316) | H | M | H | L | L
400 series (409, 430) | H | M | M | M | H
Duplex (2205) | M | H | M | H | L
OUTPUT 300 series is the pilot grade: highest exposed-finish risk and the most nickel per tonne.
Notes: Insights, stainless-specific. The six images are real output from our system on images it had never seen; each family is born at a different stage, so a typed detection goes straight to the right owner as a work order. The owner mapping needs a JSL metallurgist's sign-off in P0. Precedent: Outokumpu, Europe's largest stainless producer, switched on an AI surface inspection system at Tornio in October 2024, built to run without internet and scale across sites; Tata Steel Kalinganagar, India's first WEF Lighthouse, uses video analytics for surface defects on cold-rolled products; Parsytec systems on stainless lines use 170 micron cameras with bright and dark field light and make a decision per coil. We copy the offline edge design, an in-house team that owns the system, and the optics spec. The grade matrix output is the pilot grade: 300 series.

## Slide 4
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
Team Futuristic
IIT Bombay
Four design choices that make the system work on a real line
INSIGHTS · DESIGN CHOICES
Success is decided on the line, not in the lab: JSL's own strip, the right image detail, coil-level rules and operator trust.
Results measured by us on public steel data the system had never seen. Hardware sizing derived from our line-speed benchmark.
1 Alarms you can act on
Chart: 
| a | b
of defects caught | 89.6 | 10.4
90%
of defects caught
258 of 288 defective mill images
Chart: 
| a | b
of clean strip flagged | 4.7 | 95.3
4.7%
of clean strip flagged
14 of 300 clean mill images
So we: prove it on JSL's own clean and defective strip before any alarm is trusted.
2 One verdict per coil, not a stream of alarms
one coil, both faces: every defect with its type, size and position
ACCEPT
DOWNGRADE
HOLD
All defects on a coil roll up into one decision, using limits set per grade and finish. Example: a light scratch can pass on 2B for tubes but downgrade BA for appliance panels.
So we: agree accept, downgrade and hold limits per grade and finish with JSL Quality in P0.
3 Image detail sets what is seen, and the hardware bill
0.2 mm per pixel
~18 processors
sees defects from ~0.5 mm
0.5 mm per pixel
~3 processors
sees defects from ~1.3 mm
1.28 mm per pixel
1 processor
fine scratches vanish (~3 mm)
1.28 m strip at 250 m/min. Processors scale with pixels; a defect needs 2-3 pixels.
So we: fix the image resolution with JSL first, then size the hardware.
4 Operators act only on alarms they can trust
Every alarm shows its evidence
photo, defect type, severity and position on the coil
Four weeks of shadow mode first
it only advises; automatic holds start at ≥ 90% operator agreement
Every override is reviewed
weekly with the line and quality; the system improves from it
So we: earn trust on the shift floor before the system is allowed to act.
Notes: Four design choices. One: alarms you can act on. On real mill strip it catches 258 of 288 defects and wrongly flags only 14 of 300 clean images; the pilot repeats this on JSL's own strip before any alarm is trusted. Two: one verdict per coil. Every defect rolls up into accept, downgrade or hold, with limits agreed per grade and finish with JSL Quality. Three: image detail decides what can be seen and what the hardware costs; full detail at 250 m/min needs about 18 processing units, so resolution is a day-one decision with JSL. Four: trust is earned on the shift floor, with evidence on every alarm, four weeks of shadow mode and a weekly review of every override.

## Slide 5
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
Team Futuristic
IIT Bombay
Detect on the strip, decide at the coil, route to the owner, and learn from every correction
SOLUTION · HOW IT WORKS
Buy proven cameras, own the software: vendor-grade capture, tuned to JSL's grades and wired to JSL's process owners.
BUILT = working in our prototype today, live at surface-vision.github.io.
How it works: six stages from camera to corrective action
Capture
Both faces, bright + dark-field light, 0.2 mm detail
TO BUILD
Check
Is it usable steel? If not, skip it
BUILT
Detect
Find and classify every defect
BUILT
Score
Confidence, severity 0-100, coil position
BUILT
Decide
Accept, downgrade or hold, per grade
PARTIAL
Act & learn
Alert, hold, work order; operator feedback improves it
TO BUILD
At the line: cameras, lights
Edge server beside the line, runs offline
Plant network (IEC 62443)
People: screen, work orders
Running today
Upload a strip image, get: • box on the defect
• defect type
• confidence
• severity score
16 samples built in, including clean mill strip. Or drop your own photo.
surface-vision.github.io runs in the browser
What JSL gets that a standard system does not
Alarms you can act on
only 4.7% of clean strip raises one
Root-cause routing
every alarm becomes a work order for its owner
One verdict per coil
accept, downgrade or hold, by grade and finish
JSL owns the system
its data and software; no vendor lock-in
Build vs buy
Cost per line
Proven at speed
Tuned to JSL grades
JSL owns the system
Commercial
proven; the vendor owns it
Fully in-house
JSL owns it; slow to prove
Hybrid (recommended)
vendor cameras, JSL software
strong
partial
weak
Output: hybrid is never weak.
Notes: Solution. Stages 2 to 4 are built and running today in the browser demo. Stage 5 has coil rules built, but grade- and finish-specific limits need JSL input. Stages 1 and 6 are the plant-side pilot work. The strip underneath shows where each stage runs: cameras at the line, an edge server beside it that works offline, the plant network behind IEC 62443 zones, and people on screens and work orders. What JSL gets that a standard system does not: alarms it can act on, routing to the owning process, one verdict per coil, and ownership of its own system. Build vs buy: commercial systems are proven but closed and vendor-owned; fully in-house is slowest to prove; hybrid is never weak.

## Slide 6
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
Team Futuristic
IIT Bombay
It already works on public steel data; the pilot's job is to prove it on JSL's own strip
SOLUTION · PROOF
Strong on four of six defect families today. Every weak spot is known, and each has a fix in the pilot plan.
Datasets: NEU-DET (Northeastern Univ.); Severstal steel defects (Kaggle); GC10-DET (Lv et al. 2020, CC BY 4.0). All scores on held-out images the system had never seen.
Tested on three public steel datasets
NEU-DET
1,800 images, 6 types
University benchmark, hot-rolled strip
Severstal
12,568 real mill frames
Production strip from a steel mill
GC10-DET
2,294 frames, 10 types
Full-width line-scan camera frames (roll marks shown)
How well it finds each defect type (accuracy, held-out images)
published range
Patches
0.94
Inclusion
0.80
Scratches
0.79
Pitted surface
0.76
Rolled-in scale
0.60
Crazing
0.58
Headline results
178 of 180
test images: the right defect type named
Live
anyone can test it now at surface-vision.github.io
~10,100
Lab 1,800
Mill strip 6,001
Line-scan 2,294
Known weak spots, and the fix for each
Weak spot | Today (0-1) | Fix in the pilot
Low-contrast texture: crazing, rolled-in scale | 0.58-0.60 | Angled lighting; JSL labels in P1
Real mill frames are harder than the lab benchmark | 0.57 vs 0.75 | Prove it on JSL's own strip in P1
Roll marks and edge cracks: few examples | 0.20 | Edge cameras; targeted labelling with JSL
Notes: Proof. Three public datasets, about 10,100 images, all scored on images the system had never seen. Per defect, four of six families sit at or above the published range; crazing and rolled-in scale are low-contrast textures and are weaker. The honest headline is the second weak spot: on real mill frames the score is 0.57 against 0.75 on the lab benchmark, which is exactly why the pilot starts on JSL's own strip before anything is trusted. Roll marks score 0.20 because public data has only a few dozen examples; edge cameras and targeted labelling with JSL fix that.

## Slide 7
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
Team Futuristic
IIT Bombay
Seven months to shadow mode on one line, and nothing touches the mill until trust is earned
IMPLEMENTATION · ROADMAP · RISK
Commit one line for seven months. The month-7 go/no-go is decided on JSL's own alarm and recall numbers.
Pragati: JSL's digitalisation programme; Phase 2 brings Level-2 process data at Jajpur. KPI targets to be agreed with JSL Quality in P0.
Stage-gate roadmap (months)
m0
m4
m8
m12
m16
m20
◆ EXIT GATE
P0
Instrument one line
Optics fixed; Pragati L2 data linked
P1
Learn JSL strip (5,000 frames)
Clean alarms ≤ 25%, recall ≥ 90%
P2
Shadow mode: advises only
≥ 90% operator agreement
P3
Auto-hold on severe defects
Holds trusted; downgrade measured
P4
Second line and grade
Fleet decision on measured value
pilot go / no-go
Pilot scope: in and out
IN THE PILOT
LATER
One 300-series cold-rolled line, both faces
Hot end and caster-side inspection
2B and BA finishes
Edge cracks: needs edge cameras
Six defect families, plus unclassified
Automatic process correction
Read-only until P3; one write path
Other plants: after P4
Decision owner: JSL Quality Integration: Pragati team
Top risks, and when each is retired
Risk | Mitigation | Retired
Misses on JSL's own strip at first | Learn from JSL clean and defect images | P1
Mirror-like BA/2B finish hides defects | Bright + dark-field light; deflectometry for BA | P0-P1
Rare defects missed | Edge cameras; targeted labelling | P1-P3
Operators ignore alarms | Evidence on every alarm; shadow mode first | P2
Plant network, heat and fumes | IEC 62443 zones, runs offline; sealed enclosures | P0
Quality slips after an update | Each update must beat the live system first | P2+
Pilot KPIs: how JSL will know it works
≥ 90%
defective strip flagged
measured 258 of 288 (89.6%)
≤ 25%
clean strip wrongly flagged
measured 4.7% on mill strip
100%
coils with a defect map
design target
< 0.2 s
defect to operator screen
design target
≥ 90%
operator agreement, shadow
measured in P2
↓ vs today
downgrade rate on the line
measured in P3
Notes: Implementation. Five phases, 20 months, with a hard go/no-go at month 7 after shadow mode. The system never acts on the mill until P3; before that it only reads data and advises. The pilot scope is deliberately narrow: one 300-series cold-rolled line, both faces, 2B and BA finishes, the six defect families plus unclassified defects. The hot end, edge cracks, automatic process correction and other plants wait until the pilot has proved itself. JSL Quality owns every go/no-go; the Pragati team owns integration, because Pragati Phase 2 already brings Level-2 process data at Jajpur. Mirror-like BA and 2B finishes are handled the way stainless lines already do it: bright and dark-field light, with deflectometry for BA. The plant network is protected by IEC 62443 zones and the system runs offline. Every update must beat the live system on a fixed JSL test set before it ships.

## Slide 8
1 Problem
2 Insights
3 Solution
4 Implementation
5 Impact
Team Futuristic
IIT Bombay
At a conservative 1% downgrade rate, each line has ~₹6.7 cr a year at stake; ~₹43 cr across the fleet
IMPACT · VALUE · ASK
Recommendation: approve a 7-month pilot on one 300-series cold-rolled line. JSL's own downgrade rate decides fleet rollout.
Inputs: JSL FY26 (INR 167,407/t; 2,565,902 t sold). Base case: a 0.4 Mt line, 1% downgraded at a 10% discount. Value at stake, not a savings forecast: JSL's own data sets the real figure.
Loss pool per line, ₹ cr a year
0.4 Mt × downgrade rate × price discount × ₹167,407/t
Downgraded | 10% off | 15% off | 20% off
0.5% of volume | 3.3 | 5.0 | 6.7
1.0% of volume | 6.7 | 10.0 | 13.4
2.0% of volume | 13.4 | 20.1 | 26.8
Base case (dark): ₹6.7 cr a year per line; ~₹43 cr across JSL's 2.57 Mt. Non-prime coil sells 10-30% below prime, so these discounts are conservative.
Value levers, and how the pilot measures each
Value lever | How the system creates it | Measured in the pilot as
Fewer downgrades | defects caught upstream, before more value is added | downgrade rate by line and grade
Fewer customer claims | a defect map travels with every coil | claims per 1,000 t shipped
Less rework | no re-pickling or re-grinding of defects found late | rework tonnes per month
Faster root-cause fixes | each alarm reaches the process that caused it | hours from defect to corrective action
Premium orders | documented surface quality for rail, appliances, exports | share of exposed-finish orders
Impact beyond the P&L
Coverage
100% of both faces, every coil
today: spot checks
Customers
Defect map per coil for rail, metro, auto buyers
Vande Bharat supplier
Process
Defects tied to heat and coil IDs
6 families, each owned
Safety
Severe-defect holds prevent strip breaks
Ternium's business case
Sustainability
Less rework and remelt; backs net zero
JSL: 1.76 tCO2e/t, FY26
People
Inspectors move to decisions
HR AI: 95% self-served
WHAT WE ASK OF JSL
One 300-series cold-rolled line, 7 months
Vendor quotes for cameras and lighting in P0
Downgrade rate by line and grade
A metallurgist at 20% for root causes
In return: the measured downgrade rate, the value captured, and a go / no-go at month 7.
Notes: Impact. We size the prize, not the price. At a conservative 1% of volume downgraded at a 10% discount, one 0.4 Mt line puts about INR 6.7 crore a year at stake; across JSL's 2.57 Mt it is about INR 43 crore. Non-prime coil typically sells 10-30% below prime, so the discounts are conservative. The value comes through five levers: fewer downgrades, fewer customer claims, less rework, faster root-cause fixes, and premium exposed-finish orders. Each has a measure the pilot tracks, so the fleet decision rests on JSL's own numbers rather than our assumptions. Beyond the P&L: coverage, customers, process, safety, sustainability and people. Close on the ask.